## Slide 1
1
SATELLITE, Washington DC
Richard Jacklin, Space & Satellite Lead, March 2026
Pioneering mmWave Radar for Space Situational Awareness

## Slide 2
How does Radar work?
Emitted wave
Reflected wave
Radar works by sending out radio waves and measuring the time and strength of the echoes that bounce back from objects to determine their distance, speed, and direction.

## Slide 3
When we think about radar in space…

## Slide 4
Radar design is often making tradeoffs…
The Core Relationship Radar Equation - Monostatic

## Slide 5: Space Debris Threat
ESA's latest Space Debris Environment Report estimates 140 million untracked small debris pieces in LEO, posing a significant threat to satellite and spacecraft
The risks escalate as debris increases . . .
. . . and the debris is increasing!
Source: Space Environment Statistics · Space Debris
1 gram debris fragment in LEO has 100x more destructive kinetic energy than a 9mm bullet on Earth

## Slide 6
How comfortable does our LEO make you feel?
Today?…..
Plextek model

## Slide 7
How comfortable does our LEO make you feel?
Future?...
Plextek model

## Slide 8: mmWave FMCW RADAR
< 1mm debris detection radar

## Slide 9: CLEAR Mission & RPO RADAR
“
”
Pioneering in-orbit services for future space operations
An artistic impression of the CLEAR mission. © ClearSpace

## Slide 10
Rendezvous & Proximity Operations
Space craft need sensors to…
Know position and orientation
Navigate course trajectory and speed
Avoid hazards
Do tasks autonomously

## Slide 11
Debris removal
Docking & re-supply
Service extension
In-orbit assembly
RPO APPLICATIONS
Camera
Infra-red
LiDAR
RADAR
SENSOR TECHNOLOGIES
Un-cooperative targets
Darkness / eclipse – visibility
Darkness / eclipse – power
Obscured FoV – plume / thruster
Reliability for autonomous operation
SENSOR CHALLENGES
Sensors are critical enabler, technology and component of a ~$4.4bn market* (*Satellite Catapult estimate for 2030)
$$$
Snapshot of Sensors for Rendezvous & Proximity Operations
Rendezvous and Proximity Operations (RPO) are critical components of space missions involving two or more spacecraft that must SAFELY approach, align, and interact in orbit.
Final Approach <10m
Proximity Operations <2km
Far-Field >2km

## Slide 12
 | Camera | LIDAR | RADAR
Energy efficiency | ↑ High | ↓ Low | → Medium
Construction | → Optical | → Optical (typically moving parts) | ↑ Solid state
Detects range and velocity | ↓ No | ↑ Yes | ↑ Yes
Range vs accuracy | ↓ No | ↑ Best | → Good
Detection range | ↓ Short | ↑ Medium to Long | ↑ Medium to Long
Detection in dark / eclipse | ↓ No | ↑ Yes | ↑ Yes
Detection through dust and rocket plume | ↓ No | ↓ No | ↑ Yes
Sensing technologies: The options

## Slide 13: Rendezvous & Proximity Operations (RPO) RADAR
RPO RADAR Typical SWaP
Frequency: 60 to 80 GHz
Footprint: 15 x 10 x 5 cm
Weight: 250 gram
Power: < 10W average

## Slide 14
Lunar Lander
mmWave Radar Solutions

## Slide 15
Landing on the Moon
Why is radar good for helping space craft land on the moon?
Accurate altitude
Accurate velocity
Requires no visual clues
Can work in darkness
Can work through dust and rocket plume

## Slide 16: Example Lunar Lander Radar (3N + 1R)
4 sensors:
X, Y & Z
Altitude & Doppler
60 GHz Frequency
Each sensor:
5 to 40 degrees FoV
200 gram
~ 10 W
10Hz update rate

## Slide 17: Regolith / Dust
Particle Size Distribution (PSD) = 100 nm and 1 µm diameter
mmWave radar = 1 mm to 10 mm, therefore PSD will have little effect / backscatter
Optical LIDAR = 750 nm and 1.5 µm, wavelength similar to PSD, a big problem with high backscatter

## Slide 18
Plextek PLX-T60
60GHz mmWave radar
Drone platform
RADAR & LIDAR
Clear & smoke condition
Simulated landing

## Slide 19: Plextek Services Limited
Over 35 years heritage designing and delivering RF communications and radar-based technology solutions
Address many markets including; Defence, MedTech, Automotive and Space & Satellite
Cambridge, UK ~90 FTE Many spinouts including Blighter, Redtail, Telensa

## Slide 20: Space Market Capabilities in Radar
Rendezvous & Proximity Operations
Lunar landing & terrain
Debris monitoring in LEO
Terrain (SAR)
APPLICATION
Range, position, Doppler
Pre-processed or raw streaming
DATA
Discrete and SoC
X-band to mmWave
PLATFORMS
Tx / Rx RF Front End
Antenna development
Phased array / beamforming
RADIO INTERFACE
Lunar Landing
Lunar Terrain Vehicle Navigation
Rendezvous and Proximity Operations
Debris
Detection
Synthetic Aperture Radar
Synthetic Aperture Radar
Downstream
Midstream
Upstream

## Slide 21: Space Market Capabilities in Communications
Local and cloud based
Secure communications
APPLICATION
L2 – L3 stack development
PROTOCOL
DSP / FPGA signal processing
PHY
Comms routing
Hardware optimisation
AI / ML
Tx / Rx RF Front End
Antenna development
RADIO INTERFACE
Inter-satellite Communications
and Routing
GNSS Denied
Solutions
Telemetry, tracking
and Control
Non-Terrestrial Network
Communications
Downstream
Midstream
Upstream

## Slide 22
See a live demonstration on Plextek’s booth 1251
Richard Jacklin richard.jacklin@plextek.com +44 7801 398 701
Download our technical paper
Thank you